Quantum dot – design lasers

( http://nanohub.org/tools/qdot )

SungGeun Kim

Problem Background

Quantum dots have many applications in optical devices like lasers, photodetectors. Because the size of quantum dots can be controlled in a nanometer scale, quantum dot lasers can be tuned to emit a certain wavelength of light. For example, one can create a quantum dot laser emitting ultraviolet (UV) light, visible light, or infrared (IR) light by controlling the size of the quantum dot.

z

y

x

Fig. 1 cylindrical quantum dot.

- Using the quantum dot lab tool on nanoHUB, design a GaAs quantum dot laser with a cylindrical shape that can emit IR light (wavelength ~2400 nm) to z-direction.

(hint: start from an analytical calculation of the electron transition energy from the first excited state to the ground state and pick the proper dimension for the z direction and tune it in the tool by running simulations.)

- Predict the wavelength shift when InAs material is used instead of GaAs material for the same structure as that in problem 1. Run  a simulation using the quantum dot lab tool and compare the result with your prediction.

Useful constants:

- Planck constant 6.626 × 10-34 m2 kg / s

- Speed of light: 3 × 108 m / s

- electron charge 1.602 × 10-19 C