## Slide 1: Device Simulation: Transport (Double Gate MOSFETs)
Mehdi Salmani Jelodar, Seung Hyun Park,
Zhengping Jiang, Tillmann Kubis,
Michael Povolotsky, Jim Fonseca,
Jean Michel Sellier, Gerhard Klimeck
msalmani@purdue.edu
Network for Computational Nanotechnology (NCN)
Electrical and Computer Engineering
Purdue University
Network for Computational Nanotechnology (NCN)
1

## Slide 2
Outline
  Device Modeling Approach
Device Simulation Test Samples
  Device structure
  Sample input decks: input parameters description
  Output files and MATLAB scripts
    *.VTK files: structures / charge distribution
    MATLAB scripts: Extract ON-current, S.S, and DIBL from I-V characteristics
Band structure calculation and effective mass extraction

## Slide 3
Device Modeling Approach
m* from Full Band / Literature,
Band offset, Electron affinity
2-D / 3-D NEGF (or transfer matrix) & Poisson Solver:
Effective Mass Approximation
Like: ID-VG characteristics,
Charge distributions
Extract Device Performance Parameters:
ON-current, S.S, and DIBL
Input
NEMO5
Output
Post Processing
SS=60
ION

## Slide 4
TCH
LCH
LS
LD
5nm
11nm
10nm
10nm
Source
Drain
Si Channel
Gate
SiO2
SiO2
LS
LD
TOX
Simulation Features (ITRS 2020):
Channel material: Si
SiO2 as dielectric material
Channel length / thickness : 11 nm / 5nm
Doping concentration: 1e20 cm-3
Device Simulation Set-Up
Tox (EOT)
0.6nm
NS,D
1e20 cm-3
LCH
Gate
Si Channel
SiO2
Source
Drain
LS
LD
SiO2
Gate
LCH
TOX
TCH

## Slide 5
Required Files on Workspace
1. Go to:
/apps/share64/nemo/examples/current/public_examples/TransportDG/
Subfolders:
  MatlabFiles
  TB2EMInputDecks
  TransportInputDecks
  outputs_VD005
  outputs_VD068

## Slide 6
Device Simulation Test Samples
  Read the sample input deck: ./TranportInputDecks/inputDeckMetaDG.in
Structure:
First block defines tag, material, crystal structure, and lattice size
Second block addresses effective masses (mx, my, mz), also multi-valley can be defined by using multiple delta
In third block, band gap can be modulated.
Fourth block defines doping type (N/P), and doping concentration.
Also, different region number must be assigned to each material.
3 effective masses (m*_delta1, m*_delta2 and m*_delta3) are for 6 degenerate valleys.

## Slide 7
Device Domain
Device Domain:
In the first block, the domain name, type can be defined.
base_material is the channel material for the central of device.
passivation_regions is for the oxide areas in case of necessary (TB usage)
In second block, dimension creates a canvas of “unit cells”, representing total dimension.
periodic sets a “false” refers to a confined axis along k direction.

## Slide 8
Device Domain (cont.)
Device Domain:
In the first block, the coordinate system within the crystal_direction can be set up.
In space orientations first one is the first entry of periodic option. Only 2 directions need to be specified. NEMO5 computes the third using the crystal structure info.
In the second block, the starting cell coordinate is determined.
The contact and geometry description are shown in the third block. (Some output can be generated by de-commenting the output line.)

## Slide 9
Device Domain (cont.)
Device Domain:
In the first block, the domain name, type can be defined.
Same material is used for contacts -> base_material = channel
In the second block, the contact direction (lead_direction) can be specified.
“-1” indicates the direction of the incoming electrons. This means that n=1 for +x, n=-1 for -x, n=2 for +y, and n=-2 for –y.

## Slide 10
Device Geometry
Device Geometry:
Each component has an order of information as shown in the below.
Firstly, base shape of the region, and previously assigned region_number need to be addressed.
In min and max, the exact location and size can be adjusted. Unit is [nm]
Secondly, priority must be assigned for each component. This arranges the order of overlapping when the whole structure is built.
SiO2
1
Si (source)
2
Si (drain)
2
Si (channel)
2

## Slide 11
Device Geometry (cont.)
Device Geometry:
Top and bottom gates must be defined as same way as other components.
However, Boundary_region must be used as the tag for contacts instead of Region used in the other components.
The gates (min and max) are normally sandwiching the insulator (SiO2) and channel regions.

## Slide 12
NEMO5 Meta-Solver (1)
Meta-solver:
First it determines the solver’s name and type. By type NEMO5 will look for “MetaUTBTransport.py” in . / Meta
In transport_type it can be transfer_matrix or NEGF. For EM modeling usually transfer_matrix is faster.
We need to determine transport domain, active regions, prefix of of all output files names and as many contacts we have in the device.
In the second part, the applied voltages to source, drain and gate(s) are set up.

## Slide 13
NEMO5 Meta-Solver (2)
In first unit:
Poisson will provide the potential otherwise it will be zero.
tb_basis will determine the type of tight-binding basis should be used
Charge_self_consistant make it self-consistent with the NEGF or semi-classical (by turning on use_semiclassical_potential)
In second unit:
Number_of_enegry_points and numbe_of_momentum_points determine the number of E and K.
Momentum_intervals determines the region of calculations in Brillouin Zone.
Momentum_space_degenracy determines the degeneracy factor (2 for degeneracy and 2 for making the k region just in positive space)

## Slide 14
NEMO5 Meta-Solver (3)
output will provide the required output files during the simulation and some of these info will be stored in the VTK files
output_along_path and path_points and number_of_path_points tell the simulator to dump out only information along the path with the #points precision.
enable_structure makes the structure VTK file.

## Slide 15
Outputs with VTK files
X [nm]
Y [nm]
X
Y
Device Schematic
VTK files:
*.VTK file is created in the beginning of the simulation.
The device structure can be checked by using the VTK file in Paraview / Visit.
Charge density profile for each bias points can be obtained and checked.
X [nm]
Y [nm]
Source
Channel
Drain
Insulator
0nm
31nm
0nm
6.2nm
Off state
On state
Electron Density [/cm2]
For regions load into visit/paraview DG2020_structure.vtk
For charge density ./outputs_VD068/DG_Ramper_X.vtk

## Slide 16
Output files and MATLAB scripts
Si
DG UTB
75
5900
S.S [mv/dec]
DIBL [mV/V]
ION [μA/μm]
78
ID [μA/μm]
VGS [V]
Gate
Si Channel
SiO2
Source
Drain
SiO2
Gate
X
Y
X[nm]
Conduction Band edges
ID-VG Characteristics

## Slide 17
ION = ID (VGS = VDS)
MATLAB scripts (1)
-- > Load required files and set the variables:
clear all;clc;close all;
DIR1 = ‘../outputs_VD068/'
DIR2 = ‘../outputs_VD005/'
IVVdd = load([DIR1 ‘DG_Ramper_current.dat']);
IVV05 = load([DIR2 ‘DG_Ramper_current.dat']);
Vdd = 0.68;
IdOff = 0.1; %Set the off current to 100nA/mum as ITRS
Vg = IVVdd(:,5);
Id = 1e6*IVVdd(:,4); %convert the current from Ampere to micro-Ampere
Id05 = 1e6*IVV05(:,4);
Id05 = Id05(1:length(Id));
%% Calculate Ion
VdOff = interp1(Id,Vg,IdOff,'cubic');
Ion = interp1(Vg,Id,VdOff+Vdd,'cubic')

## Slide 18
SS = (V2-V1)/log(I2/I1) [mV/dec]
DIBL = (V2-V1)/(VDS2-VDS1)
MATLAB scripts (2)
%% Calculate SS
[a b] = find(Id>=0.1);
SS = 1000*(Vg(a(2)) - Vg(a(1)))/log10(Id(a(2))/Id(a(1)))
%% Calculate DIBL
Idibl = 1; %Current is set to 1muA/mum
Va = interp1(Id,Vg,Idibl,'cubic');
Vb = interp1(Id05,Vg,Idibl,'cubic');
DIBL = 1000*(Vb-Va)/(Vdd-0.05)
%% Plot IV
figure(1);hold on;box on;axis square;grid on;
plot(Vg,Id,'b','linewidth',3);
plot(Vg,Id05,'r','linewidth',3);
set(gca,'YScale','log'); hold off;
ID [μA/μm]
VGS [V]
ID-VG Characteristics

## Slide 19
MATLAB scripts (3)
%% Plot conduction band
figure(4);hold on;box on;axis square;grid on;
for ii =1:N
XY = load ([DIR1 ‘DG_Ramper_' int2str(ii-1) '.xy']);
plot(XY(:,1), XY(:,3), '-b','LineWidth',2.5); %Conduction band
end
X[nm]
Conduction Band edges

## Slide 20
Transport effective mass
What is effective mass (m*)?
  It is determining how easily an electron moves in a material in specific condition (like direction, temperature and pressure)
  where
How to find m*?
  Measure in a lab
  DFT calculations (from band structure)
  Tight binding approach (from band structure)

## Slide 21
Band structure calculation with N5 (input deck)
Determine the material (s)
  Material (InAs)
  Parameter set (param_Klimeck)
Domain
  Periodicity (periodic = (true, true, true))
Solver
  Type (Schroedinger)
  Set the K space
  k_space_basis = reciprocal
  k_points = [(0.1,0.1,0.1),(0.0,0.0,0.0),(0.1,0.0,0.1)]
  number_of_nodes = (21,21)
Calculate the effective mass (run the Matlab script TB2EM.m)
 Please look at ./TB2EMInputDecks/InAs_TB2EM.in

## Slide 22
Load InAs_k_distance;
load InAs_energies; plot(InAs_k_distance,InAs_energies);
box on; axis square;
Effective mass calculations:
a = 6.0583;%e-010; %[m]
hBar = 1.0546e-034;
q = 1.60217646e-19;
m0 = 9.10938188e-31;
EE = Energies(21:25,9);
dK = diff(K_distance(21:22));
EK = (EE(1)+EE(3)-2*EE(2))/((dK)^2);
mStar = (hBar^2)/EK/q/m0/1e-18;
 Please run the Matlab script ./MatlabFiles/TB2EM.m
Extracting effective mass for InAs bulk
X
L

## Slide 23
Effective mass – non-parabolicity
figure(1); %Plot parabolic EK
plot(K_distance,Energies,'k','linewidth',2.5);
axis square; box on;ylim([-1 2]);
K_points = load([x '_k_points.dat']);
K = sum(K_points.^2,2);
E = (hBar^2/mStarGamma/2/q/m0/1e-18)*K;
hold on;
H3 = plot(K_distance,E+0.5942,'s-b');
ENP = (-1+sqrt(1+4*alpha*E))/(2*alpha);
H4 = plot(K_distance,ENP+0.5942,'o-r');
X
L

## Slide 24
Extracting effective mass for InAs sheet
Domain
  Periodicity (periodic = (true, true, false))
Solver
  Set the K space
  k_points = [(0.0,0.5),(0.0,0.0),(0.5,0.0)]
  number_of_nodes = (21,21)
Calculate the effective mass
  (run the Matlab script TB2EM.m)

## Slide 25
Thank you!
Questions/feedback send me email to:
msalmani@purdue.edu

## Slide 26
Current (I-V)
Capacitance(C-V)