## Slide 1: Lecture: Tunnel FET
Mark Cheung
Department of Electrical and Computer Engineering,
University of Virginia, Charlottesville, VA 22904, USA

## Slide 2: This lecture will cover:
Field-effect transistor (FET) review
Motivation for TFET
Device design and simulation
Literature review
Simulation results

## Slide 3: Field-effect transistor (FET) review
Switch
  On: ID is high
  Off: ID is low
Landauer Formula:

## Slide 4: Motivation
"Intel," 2011. Available: http://www.carthrottle.com/why-chemistry-dictates-an-electric-vehicle-future/

## Slide 5: Current-voltage (IV) curve
Subthreshold Swing SS (mV/dec):
Power P=(1/2)C+VdIloff
Ioff
Ion
~60 mV/dec
MOSFET IV Curve
≈ 60 mV/dec

## Slide 6
Tunnel Field Effect Transistor (TFET)

## Slide 7: Tunnel Field Effect Transistor (TFET)
Off
On
q∆
λ
Channel
Source
Drain
Notes: The theoretical limit of the mosfet transistor that is the most popular one today 60mV/dec. In my research, I look into another kind of transistor: TFET. Here is the energy band diagram of TFET.
The blue line is for the off state and red line is the on state. In the off state, tunneling is much harder because no empty states in the channel are available and the length of channel is long to minimize Id,off. Increasing Vg above a certain threshold moves the valence band energy (𝐸_𝑣^𝑐ℎ) of the channel above the conduction band energy (𝐸_𝐶^𝑆) of the source so that interband tunneling can occur (green arrow). This switches the device to the on state, in which electrons in the gap (∆Φ=𝐸_𝑣^𝑐ℎ−𝐸_𝐶^𝑆) can tunnel from the source conduction energy levels into the channel valence energy levels as the gap (λ) is small. The amount of current jumped after a threshold (q∆𝑉_𝑔). In other words, a low subthreshold swing (less than 60mV/decade limit for a MOSFET) can be achieved. See equation

## Slide 8: Device design and simulation
Source
Drain
Gate
[H]

## Slide 9: Graphene Nanoribbon (GNR)
Subbands
Transmission

## Slide 10: Relevant Functions (analytical)
  SS=
J. Knoch, S. Mantl and J. Appenzeller, "Impact of dimensionality on the performance of tunneling FETs: Bulk versus one-dimensional devices," ScienceDirect, vol. 51, pp. 572-78, 2007.

## Slide 11: Literature Review: MOSFET/TFET IV of different material system
A. M. Ionescu and H. Riel, "Tunnel field-effect transistors as energy-efficient electronics switches," Nature, vol. 479, pp. 329-337, 2011.

## Slide 12: Literature Review: varying gate overlap & differential voltage
Gate overlap improves SS
without degrading Ion and Ioff
Differential voltage between top and bottom gate
for a double gate TFET correlates positively with Ion/Ioff
Fiori, G.; Iannaccone, G., "Ultralow-Voltage Bilayer Graphene Tunnel FET," Electron Device Letters, IEEE , vol.0, no.10, pp.1096,1098, Oct. 2009 doi: 10.1109/LED.2009.2028248
Notes: Similar physics in bilayer graphene

## Slide 13: Literature Review: varying drain-side gate underlap & drain doping
X. Yang, J. Chauhan, J. Guo, and K. Mohanram “Graphene tunneling FET and its applications in low-power circuit design,” VLSI, pp. 263-268, 2010
Drain-side gate underlap and drain doping reduce the
ambipolar IV characteristics without sacrificing Ion/Ioff and SS

## Slide 14: Result: varying channel width
Channel width varies inversely with SS and correlates negatively (exponential) with Ion/Ioff
Notes: Transistors of width <3.75nm do not generate enough on-current.

## Slide 15: Result: varying channel width
Chart: width (nm)
| 1.25 | 2.5 | 3.75 | 5 | 6.25 | 7.5
SS (mV/dec) | 234 | 96.8 | 33.9 | 20.4 | 15.8 | 6.02
Ion/Ioff | 153846.1538 | 7142.8571 | 1645.5696 | 50.4
Ion/Ioff2 | 100000 | 1000
Channel width varies inversely with SS and
correlates negatively (exponential) with Ion/Ioff
Notes: Transistors of width <3.75nm do not generate enough on-current.

## Slide 16: Results: varying channel length
Off
On
q∆
λ
Channel
Source
Drain

## Slide 17: Results varying channel length
Chart: length (nm)
| 10 | 20 | 40 | 80 | 160
SS (mV/dec) | 160 | 34.3 | 20.4 | 20.4 | 20.4
Ion/Ioff | 13.8889 | 892.8571 | 71428.5714 | 71428.5714 | 71428.5714
Channel length varies inversely with SS and
correlates positively (logarithmic) with Ion/Ioff

## Slide 18: Results: varying doping in contacts
Channel doping correlates positively with SS (exponential) and
positively with Ion/Ioff (exponential) up until doping of around 0.28eV
Off
On
q∆
λ
Channel
Source
Drain

## Slide 19: Results: varying doping in contacts
Chart: doping (eV)
| 0.2 | 0.22 | 0.24 | 0.28000000000000003 | 0.32 | 0.36
SS (mV/dec) | 5.8 | 6.1 | 6.5 | 8 | 29.7 | 64.8
Ion/Ioff | 10571.0955 | 31748.8381 | 76096.339 | 155368.0436
Ion/Ioff2 | 738.778 | 197.2626
Channel doping correlates positively with SS (exponential) and
positively with Ion/Ioff (exponential) up until doping of around 0.28eV

## Slide 20
Results: varying drain bias
Drain bias correlates positively with SS (linear & weak)
and negatively with Ion/Ioff (exponential)
Off
On
q∆
λ
Channel
Source
Drain

## Slide 21
Results: varying drain bias
Chart: vd (V)
| 1E-3 | 0.01 | 0.05 | 0.1 | 0.15 | 0.2
SS (mV/dec) | 6.8 | 5.6 | 7.7 | 6.5 | 9.2 | 10.8
Ion/Ioff | 200000 | 243750 | 158730.1587 | 50000 | 7000 | 1125
Drain bias correlates positively with SS (linear & weak)
and negatively with Ion/Ioff (exponential)

## Slide 22: Conclusion
SS of 6.4 mV/dec and Ion/Ioff of >25,000 were obtained for length=40nm, width=5nm, vd=0.1 V, and doping=0.24eV.
Further analysis is required to balance the trade-offs among size, power, and performance.
In comparison to a MOSFET, high Ion/Ioff ratio and steep SS over several decades indicate GNR TFET’s superiority for ultra-low-voltage applications.

## Slide 23: Future direction
Link experimental results with analytical equations
Adjust simulation to account for experimental challenges
  Include scattering (inelastic & elastic)
Alternative TFET designs

## Slide 24: Appendix: Simulation Design (continue)
Tight-binding Hamiltonian model
TFET setup:
  Channel doping
  Tri-gate
Non-equilibrium green function (NEGF)
Assumptions:
  Room temperature
  ballistic transport
  electrodes are infinite electron reservoir
  steady state
Notes: E : energy matrices from the electronic band structure
H : hamiltonian matrix
〖"Σ " 〗_1,2 : self energy matrices from the contacts
To analyze quantum transport, we need an integration of quantum mechanics described by the Schrödinger Wave Equation. This is achieved in the paper using NEGF method.
I will not go into much detail as to do so require quantum mechanics, complex variables, matrix algebra, etc. I will just give you a general overview of some algorithms that are the focus of the paper.

## Slide 25: Appendix: NEGF
  E : energy matrices from the electronic band structure
  H : hamiltonian matrix
  : self energy matrices from the contacts
    = , =
    : broadening matrices due to coupling with contacts
    f: fermi functions describing number of electrons
  Electron density per unit energy

## Slide 26: Appendix: NEGF (continue)
T(E)=Trace()
  Average transmission at different energy
U=
  Potential energy effecting the DOS , and hence the transmission T
  )+)
  Probability that an electron will be at an energy state E given the fermi level , and temperature T

## Slide 27: Appendix: Relevant functions (continue)
  SS=
J. Knoch, S. Mantl and J. Appenzeller, "Impact of dimensionality on the performance of tunneling FETs: Bulk versus one-dimensional devices," ScienceDirect, vol. 51, pp. 572-78, 2007.