## Slide 1
Understanding Variation and Statistical Process Control:
Variation and Process Capability Calculations

## Slide 2: Outline
Variation and It’s Relationship to Quality
The Normal Distribution as a Model for Describing Variation
Comparing Variation to Specifications
Relationship between Cp and Cpk
Calculation of Cpk and Ppk

## Slide 3: New Face of Quality – Low Variation
Quality = possessing one or more functional characteristics that improve the performance of a product or service. i3 vs i5 has lower # of cores, low cache memory and no Turbo Boost for speed.
Michael Close is developing an addition process to adjust each batch of incoming raw material to the same acetate content before being released into production. -- I don’t care where they set it, I just wish it would stay the same! --
Carbon Nanotubes are a true example of nanotechnology, embodying a unique combination of electrical, thermal, and structural properties. Helix’s state-of-the- art chemical vapor deposition (CVD) process enables the production of nanotubes with controlled Diameter (1.2 ~ 1.5 nm diameter ) which is critical to those physical properties.

## Slide 4: Data from the Process Provides Variation Insight
Since the physical properties of carbon nanotubes are a function of it’s volume
/ surface area ratio, the diameter of the nanotubes is a key quality characteristic.

## Slide 5: A Histogram Outlines the Diameter Distribution
1.60
1.52
1.36
1.28
1.20
25
20
15
10
5
0
1.44
Diameter
Frequency
Histogram of Diameter

## Slide 6: A Normal Distribution defines the Diameter Variation
1.60
1.52
1.36
1.28
1.20
25
20
15
10
5
0
Mean 1.393
StDev 0.05673
N 60
1.44
Diameter
Frequency
Histogram of Diameter

## Slide 7: Data Assumed as a Sample of a Normal Population
Probability of a nanotube diameter of 1.36 or less is about 18%.
Assuming a normal population distribution allows calculation of probabilities of interest.
Mean = 1.393 mm
Std Deviation = .0567 mm

## Slide 8: Assuming a Normal Distribution Establishes Limits
1.6
1.5
1.3
7
6
5
4
3
2
1
0
1.2
1.4
Diameter
Probability
- 3*Sigma
+ 3*Sigma
99.7% of the data will fall between + / - 3 sigma 95.5% of the data will fall between + / - 2 sigma 68.3% of the data will fall between + / - 1 sigma
- 2*Sigma - Sigma Mean + Sigma + 2*Sigma

## Slide 9: Cp to Measure Process Capability
1.8
1.7
1.6
1.5
1.3
1.2
1.1
1.0
7
6
5
4
3
2
1
0
1.4
Diameter
Probability
Mean
Lower Specification
Upper Specification
Mean=1.393 StDev=0.05673
Is my process capable of meeting my customers specs?
Cp = (Upper Spec – Lower Spec) 6 * Standard Deviation

## Slide 10: Cp to Measure Process Capability
1.8
1.7
1.6
1.5
1.3
1.2
1.1
1.0
0.0
1.4
Diameter
Probability
Upper Specification
Lower Specification
1.8
1.7
1.6
1.5
1.3
1.2
1.1
1.0
0.0
1.4
Diameter
Probability
Lower Specification
1.8
1.7
1.6
1.5
1.3
1.2
1.1
1.0
0.0
1.4
Diameter
Probability
Lower Spec
Upper Spec
Uncapable Process - Cp = .70
Mean
Mean=1.393 StDev=0.05673
5.0
2.5
Just Capable Process - Cp = 1.0
Mean Upper Specification
Mean=1.393 StDev=0.05673
5.0
2.5
Very Capable Process - Cp = 1.5
Mean
Mean=1.393 StDev=0.05673
5.0
2.5

## Slide 11: Cp to Measure Process Capability
2.1
2.0
1.9
1.8
1.7
1.4
1.3
1.2
1.1
1.0
7
6
5
4
3
2
1
0
1.5 1.6
Diameter
Probability
Mean Lower Specification
Upper Specification
Mean=1.393 StDev=0.05673
Is my process capable of meeting my customers specs?
Cp = (Upper Spec – Lower Spec) 6 * Standard Deviation

## Slide 12: Process Capability
Cpk = min [ (Upper Spec – Avg) or (Avg - Lower Spec) ]
3 * Standard Deviation
1.8
1.7
1.6
1.5
1.2
1.1
1.0
7
6
5
4
3
2
1
0
1.4
Diameter
Probability
Mean
Lower Specification
Upper Specification
Mean=1.393 StDev=0.05673
Target
1.3

## Slide 13: Process Capability Calculations
Cp = (Upper Spec – Lower Spec)
Process Variation
Cpk = min [ (Upper Spec – Avg) or (Avg - Lower Spec) ]
Half the Process Variation
Spec Range = 1.2 - 1.5 nm
Mean=1.393 StDev=0.05673
Cp = (1.5 – 1.2 ) / (6 x .0567) = .88
Cpk = (1.5 – 1.393 ) / (3 x .0567) = .63

## Slide 14: Process Capability
(Short-term and Long-term)
1
S1
S2
S3
S4
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
Std Dev Short-term = Std Dev Pooled = Std Dev (within) =
[(S1**2 + S2**2 + S3**2 + S4**2) / 4 ]
.5
Std Dev Overall
Std Dev Long-term
Ppk & Pp are Cpk & Cp with Std Dev = Std Dev Overall

## Slide 15: Data for Long-term Process Capability
Since the physical properties of carbon nanotubes are a function of it’s volume
/ surface area ratio, the diameter of the nanotubes is a key quality characteristic.

## Slide 16: Calculate the Process Capability
46
41
36
31
21 26
16
11
6
1
1.45
1.40
1.35
Sample Mean
_ X=1.4042
UCL=1.4606
LCL=1.3477
46
41
36
11
6
1
0.2
0.1
0.0
Sample Range
_ R=0.0979
UCL=0.2071
LCL=0
45
40
35
30
25
1.5
1.4
1.3
Values
1.20 1.26 1.32 1.38 1.44 1.50 1.56
Specifications LSL 1.2
USL 1.5
LSL
Overall
Within
1.6
1.5
1.4
1.3
Within StDev 0.04339
Cp 1.15
Cpk 0.74
PPM 13596.62
Overall StDev 0.04736
Pp 1.06
Ppk 0.67
Cpm *
PPM 21504.56
Overall
Within
Specs
Sample
1
6
5
2
1
Calculating long-term / short-term process capability requires;
Upper and/ or lower specifications.
Confirmation that the process is in control.
Confirmation that the process data is normally distributed.
Process data representing long-term & short-term variation.
Process Capability Sixpack Report for Diameter
Xbar Chart
1
R Chart
16 21 26 31
Last 25 Subgroups
Capability Histogram
USL
Normal Prob Plot
AD: 0.959, P: 0.015
Capability Plot

## Slide 17: Interpretation of Capability Output
Use the Capability Analysis to reach the following conclusions;
Process variation is about equal to the specs ( Pp is about = 1.0).
Process is off center ( Ppk < Pp ).
Process is fairly in control (Ppk is about = Cpk).
1.20 1.26 1.32 1.38 1.44 1.50 1.56
Process Data
LSL 1.2
Target *
USL 1.5
Sample Mean 1.40416
Sample N 240
StDev(Overall) 0.0473588
StDev(Within) 0.0433924
Potential (Within) Capability
Cp 1.15
Cpk 0.74
Overall Capability Pp 1.06
Ppk 0.67
Observed Expe % < LSL 0.00 | cted Defects 0.00
% > USL 2.92 | 1.36
% Total 2.92 | 1.36
Overall
Within
Process Capability Report for Diameter
LSL USL
Diameter

## Slide 18: Relationship Between Cpk vs Ppk vs Cp
Cpk = Ppk Cpk = Cp
Ppk < Cpk
Cpk < Cp
Cpk < Cp Ppk < Cpk
Process Centered
Process Off -Center
In Control
Out of Control

## Slide 19: Acceptable Cpk Levels
Defect Levels Associated with Cpk Values
Airline Industry -
Safety
Baggage
Cpk = 2 or more Cpk = .4 or less
Pharmaceutical Industry - Auto Industry -
Typical Manufacturing -
Cpk = 1.75
Cpk = 1.33
Cpk = 1.00
Nanoscale Manufacturing = ?

## Slide 20: Conclusions
Modern nanoscale processes seeking to produce high Quality products will seek to understand and minimize the variation in their key Quality characteristics.
Graphical analysis such as the histogram and normal probability plots allow one to understand and model the variability in process outputs.
Capability indices such as Cp and Cpk compare the process variation to the customers specifications. They are used to determine if the variation is wider than the specifications, the process is not centered or both.
If process data is collected over a long time period,
Pp and Ppk are used to determine the long-term process performance capability.