ECE 440: Solid State Electronic Devices

Fall 2008

Section E: MWF 1:00-1:50PM • Everitt 163 • Prof. Eric Pop

Course Mechanics:

- Three lecture/discussion meetings per week

- Four sections in parallel: same syllabus, homeworks, exams

- Final grade = Tests + 0.15 × (1 – Tests/100) × Homeworks

where Tests = 0.25 Midterm + 0.40 Quizzes + 0.35 Final

- Midterm → Tues, Oct 14, 7-9pm in MSEB 100

- Quizzes → approx. 6 in-class, 20 min. each, lowest dropped

- Homeworks, solutions, other resources on web site:

  - http://courses.ece.uiuc.edu/ece440

- Prof. Eric Pop, OH Monday 10-11 am, MNTL 2258

- TA: Jihan Kim, OH Friday 2-4 pm, Beckman 3253

- Feel free to attend any/all lectures and office hours

- Additional office hours by appointment

Please read Syllabus handout

Questions:

- Why “solid state”?

- Why “electronics”?

- Why are we here?

What’s at the heart of it all?

What can we get out of it?

The Abacus, Ancient Digital Memory

- Information represented in digital form

- Each rod is a decimal digit (units, tens, etc.)

- A bead is a memory device, not a logic gate

An Early Mechanical Computer

Sources: R. Cavin (SRC), Wikipedia

Ohm’s law: V = I × R

Georg Ohm, 1827

Semiconductors are not metals

Michael Faraday, 1834

Semiconductor resistance decreases with temperature

Discovery of the electron

J. J. Thomson, 1897

(measured only charge/mass ratio)

“To the electron – may it never be of any use to anybody.” – J. J. Thomson's favorite toast

Measuring the electron charge: 1.6 × 10-19 C

Robert Millikan, oil drops, 1909

Sources: Wikipedia, http://www.pbs.org/transistor

ENIAC: The first electronic computer (1946)

30 tons, including ~20,000 vacuum tubes, relays

Punch card inputs, ~5 kHz speed

It failed ~every five days

Note: ILLIAC @ UIUC

5 tons, 2800 vacuum tubes

64k memory (1952)

Modern age:

The first semiconductor transistor

AT&T Bell Labs, Dec 1947

J. Bardeen, W. Brattain, W. Shockley

Germanium base, gold foil contacts

Note: ILLIAC II @ UIUC

Built with discrete transistors (1962)

Sources: Wikipedia, http://www.pbs.org/transistor

The way I provided the name, was to think of what the device did. And at that time, it was supposed to be the dual of the vacuum tube. The vacuum tube had transconductance, so the transistor would have “transresistance.” And the name should fit in with the names of other devices, such as varistor and thermistor. And… I suggested the name “transistor.”

– John R. Pierce AT&T Bell Labs, 1948

First transistor radio Regency TR-1 (1954)

Built with four discrete transistors

Integrated circuits fabricate all transistors and metal interconnects on the same piece of silicon

- Jack Kilby UIUC’47, patent TI’1959, Nobel prize 2000

- Robert Noyce 1961, co-founder of Fairchild, then Intel

The first microprocessor, Intel 4004 (1971)

2250 transistors, 740 kHz operation

- Comparable computational power with ENIAC

- Built on 2” and then 3” wafers (vs. 12” today)

- 10 μm line width (vs. 65 nm today)

- 4-bit bus width

- Used in… the Busicom Calculator:

Followed by 8008 (8-bit), 8080, 8086

Then 80286, 80386, 80486 = i486 (1989, 0.8 μm lines)

Pentium, II, III, Itanium, IV, Celeron, Dual-Core, Core 2…

Gordon Moore’s “Law”

≈ doubling circuit density every 1.5-2 yrs

Source: http://www.intel.com

Transistor size scaling:

Sources: NSF, Intel

Some unintended (negative) side-effects of scaling:

Take off the cover of a microprocessor.

Why semiconductors?

- vs. conductors or insulators

- Elemental vs. compound

Why (usually) crystalline?

Why silicon?

Why the (CMOS) transistor?

- Transistor = switch

- Technology is very scalable (Moore’s Law)

- CMOS = complementary metal-oxide-semiconductor

- Fabrication technology = reproducible on extremely large scales

- Circuit engineering

- Design abstractions

What do we learn in ECE 440?

One shouldn’t work on semiconductors, that is a filthy mess; who knows if they really exist!

Wolfgang Pauli, 1931

(Nobel Prize, Physics, 1945)

# Text boxes

Charles Babbage (Wikipedia)

The Babbage

Difference Engine (1832)

25,000 parts

AT&T Bell Labs 1945-1951

Univ. Illinois ECE & Physics 1951-1991

F.F. = Federico Faggin

(designer)

1965

Influenza virus

“90 nm” technology

in my laptop CPU today

Full wafer (100s of dies)

Single transistor

Packaged die

Cross-section

Devices

- P-N diode

- Schottky barrier

- Bipolar junction transistor

- Metal-oxide-semiconductor field-effect transistor (MOSFET)

- Solar cells

- Photodiodes

ECE 440

Processing

- Zone refining

- Epitaxial growth

- Photolithography

- Resist (positive/negative)

- Encapsulation (CVD, sputtering)

- Ion etching

- Ion implantation and diffusion

(ECE 444)

Materials

- Fundamental properties

- Crystal structure

- Charge carriers

- Energy bands

- Optical absorption (direct/indirect)

- Electrical properties (drift/diffusion)

- Mobility and diffusion

Circuits

Physics