Test for Periodic Potential Lab

- What is the mass of electrons in vacuum?

  - m0

  - 2m0

  - 4m0

- Is the electron mass in a crystal equal to the free electron mass?

  - Yes

  - No

- How are electrons represented in a crystal?

  - As plane waves

  - With Bloch functions

  - Neither of the above

- What is the best representation of a realistic crystal potential?

  - With periodic Coulomb potentials

  - With periodic square well potentials

  - As periodic triangular potential

- Assume periodic square well potential. What happens to the width of the band when the thickness of the barrier decreases and the width of the well is kept constant?

  - increases

  - decreases

  - stays the same

- Assume periodic square well potential. What happens to the width of the bands when the height of the barrier increases and the width of the well is kept constant?

  - decreases

  - increases

  - stays the same

- It is well known that periodic crystal potential opens gaps in the dispersion relation. What happens with the width of the gaps at higher energies?

  - increases

  - decreases

  - stays the same

- Now let us consider Coulombic periodic potential. What happens to the energy gaps in this case when increasing energy?

  - Increase

  - Decrease

  - Stay the same

- It is well known that in a Coulomb potential the energy level separation decreases with increasing energy. What can we say about the width of the bands?

  - Increases with energy

  - Decreases with energy

  - Stays the same

- It is well known that once the energy band structure is determined, then the effective mass at a particular energy can be extracted as:

  - Being proportional to the curvature of the bands

  - Being proportional to the slope of the bands

  - None of the above

- Larger curvature of the bands means

  - Smaller effective mass

  - Larger effective mass

  - None of the above

- The electrons behave as almost free electrons if the square potential is such that the

  - Barrier width goes to zero

  - Barrier height goes to infinity

  - None of the above